## Slide 1
SYNTEENSYZER
Real-Time Polyphonic Synthesiser on Teensy 4.0
Projet 1A — INSA Lyon
2025 – 2026

## Slide 2
Synteensyzer — INSA Lyon 1A
2 / 11
Agenda
01
Live Demo
30 sec
02
Project Overview
2 min
03
System Architecture
2 min
04
Software Architecture
2 min
05
Technical Deep Dive
4 min
06
Challenges & Solutions
2 min
07
Conclusion & Perspectives
1 min

## Slide 3
Live Demo
Play notes — Switch presets — Record a loop
3 / 11

## Slide 4
Synteensyzer — INSA Lyon 1A
4 / 11
Project Overview
A real-time polyphonic synthesiser running on a Teensy 4.0 microcontroller.
The PC sends MIDI notes over USB, the Teensy computes the sound
and outputs it to headphones through an audio codec.
8 simultaneous polyphonic voices
4 timbres (sine, organ, electric, pad)
ADSR envelope per voice
Configurable echo/delay effect
Looper (record / play / stop)
Physical button (short / long press)
Tech Stack
Teensy 4.0 (ARM 600 MHz)
Audio Shield SGTL5000
C++ / Arduino
USB MIDI Protocol
PlatformIO

## Slide 5
Synteensyzer — INSA Lyon 1A
5 / 11
System Architecture
PC
MIDI Keyboard
(virtual or physical)
USB MIDI
Teensy 4.0
MIDI Reception
DSP Engine (C++)
8-voice polyphony
ADSR + Echo
I2S
Audio Shield
SGTL5000 DAC
Headphone output
44,100 Hz
Sample Rate
128 samples
Block Size
600 MHz ARM
CPU
512 + 512 KB
RAM

## Slide 6
Synteensyzer — INSA Lyon 1A
6 / 11
Software Architecture
One file = One responsibility
MyDsp
Audio engine
8 voices + ADSR + Echo
Real-time DSP
Looper
Record & replay
MIDI events
State machine
MidiHandler
Route MIDI
messages
Protocol routing
Button
Debounced input
short/long press
Embedded I/O
main.cpp
Wire modules
together
Orchestration
config.h
Shared
constants
Single source

## Slide 7
Synteensyzer — INSA Lyon 1A
7 / 11
Real-Time Audio Synthesis
Hard real-time constraint: update() must complete within 2.9 ms or the audio glitches
Audio Pipeline (per block of 128 samples)
8 Voices
▶
Oscillator
▶
ADSR
Envelope
▶
Mix
▶
Echo
(delay)
▶
Soft Clip
▶
I2S Out
4 Timbres (Presets)
Sine
Pure wavetable lookup
Organ
Additive: f + 2f + 3f + 1.5f
Electric
Harmonics + noise transient
Pad
Detuned sines + low-pass filter

## Slide 8
Synteensyzer — INSA Lyon 1A
8 / 11
The Looper — State Machine
EMPTY
RECORDING
PLAYING
STOPPED
short
press
short
press
short
press
long press (3s) → CLEAR → back to EMPTY
Key Design Decisions
Events stored as {timestamp, type, note, velocity}
Replayed in real-time by comparing elapsed time to event timestamps
Preset is "frozen" at record start — loop keeps its timbre
Fixed buffer of 2048 events (no dynamic allocation on embedded)

## Slide 9
Synteensyzer — INSA Lyon 1A
9 / 11
ISR / Main Loop Concurrency
The Problem
Audio ISR (every 2.9 ms)
update() reads voices[], preset, echo params
Main loop() (continuous)
noteOn/Off/setters write voices[], preset, echo
⚠ Same data, no protection = DATA RACE
The Solution
__disable_irq();
// ... modify shared state ...
// (voices, preset, gain, echo)
__enable_irq();
Standard Teensy Audio Library pattern.
Critical section is tiny (< 1 µs) — no impact on audio latency.

## Slide 10
Synteensyzer — INSA Lyon 1A
10 / 11
Challenges & Solutions
Monolithic code (400 lines in one file)
→
Restructured into 5 focused modules
Audio glitches during note changes
→
Added ISR protection (__disable_irq / __enable_irq)
Looper lost timbre on preset switch
→
Preset "freeze" at recording start
DSP too slow (powf() called per sample)
→
Cached phaseInc in noteOn() — compute once

## Slide 11
Conclusion
✓
Fully working polyphonic synthesiser
✓
Real-time audio on embedded hardware
✓
Clean modular architecture (5 modules, 800 lines)
✓
MIDI-controlled with looper functionality
Perspectives
→ True stereo output (L/R panning)
→ ADSR controllable via MIDI CC
→ Loop quantisation (snap to tempo)
→ PC graphical interface
Synteensyzer — INSA Lyon 1A
11 / 11